## Slide 1: Mediator

## Slide 2: Functions
承上启下，屏蔽模块
承上：Orchestration、Measurement
启下：各种模块。有两种模式：
  第一种（期刊使用）：Ryu controller、Classifier Controller、BESS Controller、Docker Controller、Server Manager
  第二种（项目使用）：P4 controller、BESS Controller、Docker Controller、Server Manager

## Slide 3: Requirement
模式可配置
根据命令（add/del sfci，get topology, get server sets, get vnfi state）向相应的控制器发送指令。
纯P4网络
P4和Server都可以部署NFs
Classifier用P4实现

## Slide 4: Design
读取系统配置：
  交换机：P4/OpenFlowSwitch（项目里面只用P4）
    这个会影响将command发给P4controller还是SDNcontroller
  网络控制器：ONOS/FLOODLIGHT/RYU （项目里面只用ONOS）
    从RYU_QUEUE、ONOS_QUEUE 、FLOODLIGHT_QUEUE中选择
  Classifier：P4/Server（项目里面只用P4）
    Command发给：P4_QUEUE, SERVER_CLASSIFIER_CONTROLLER_QUEUE
截取command和commandReply，修改并转发

## Slide 5: WorkFlow1- SDN switch
Input:
  MSG_TYPE_MEDIATOR_CMD
    get CMD_TYPE_ADD_SFCI from orchestration
Process:
  Store this command, its state: (state, state, state, state)
  先发送给bessController；再发送dockerController，需要state状态机的转换
Output:
  MSG_TYPE_NETWORK_CONTROLLER_CMD
    CMD_TYPE_ADD_SFCI to networkController
  MSG_TYPE_CLASSIFIER_CONTROLLER_CMD
    CMD_TYPE_ADD_SFCI to classifierController
  MSG_TYPE_BESS_CONTROLLER_CMD
    CMD_TYPE_ADD_SFF to bessController
  MSG_TYPE_DOCKER_CONTROLLER_CMD
    CMD_TYPE_ADD_SFCI to dockerController

## Slide 6: WorkFlow1 – P4 switch
Input:
  MSG_TYPE_MEDIATOR_CMD
    get CMD_TYPE_ADD_SFCI from orchestration
Process:
  Store this command, its state: (state, state, state)
  先发送给bessController；再发送dockerController，需要state状态机的转换
Output:
  MSG_TYPE_NETWORK_CONTROLLER_CMD
    CMD_TYPE_ADD_SFCI to networkController
  MSG_TYPE_CLASSIFIER_CONTROLLER_CMD
    CMD_TYPE_ADD_SFCI to classifierController
  MSG_TYPE_BESS_CONTROLLER_CMD
    CMD_TYPE_ADD_SFF to bessController
  MSG_TYPE_DOCKER_CONTROLLER_CMD
    CMD_TYPE_ADD_SFCI to dockerController

## Slide 7: WorkFlow2- SDN switch
Input:
  MSG_TYPE_MEDIATOR_CMD
    get CMD_TYPE_DEL_SFCI from orchestration
Process:
  Store this command, its state: (state, state, state, state)
Output:
  MSG_TYPE_NETWORK_CONTROLLER_CMD
    CMD_TYPE_DEL_SFCI to RyuController
  MSG_TYPE_CLASSIFIER_CONTROLLER_CMD
    CMD_TYPE_DEL_CLASSIFIER_SFCI to classifierController
  MSG_TYPE_BESS_CONTROLLER_CMD
    CMD_TYPE_DEL_SFF_SFCI to bessController
  MSG_TYPE_DOCKER_CONTROLLER_CMD
    CMD_TYPE_DEL_VNFI to dockerController

## Slide 8: WorkFlow2- P4 switch
Input:
  MSG_TYPE_MEDIATOR_CMD
    get CMD_TYPE_DEL_SFCI from orchestration
Process:
  Store this command, its state: (state, state, state)
Output:
  MSG_TYPE_NETWORK_CONTROLLER_CMD
    CMD_TYPE_DEL_SFCI to networkController
  MSG_TYPE_CLASSIFIER_CONTROLLER_CMD
    CMD_TYPE_DEL_CLASSIFIER_SFCI to classifierController
  MSG_TYPE_BESS_CONTROLLER_CMD
    CMD_TYPE_DEL_SFF_SFCI to bessController
  MSG_TYPE_DOCKER_CONTROLLER_CMD
    CMD_TYPE_DEL_VNFI to dockerController

## Slide 9: WorkFlow3
Input:
  MSG_TYPE_MEDIATOR_CMD
    get CMD_TYPE_GET_SERVER_SET from measurement
Process:
  Store this command, its state
Output:
  MSG_TYPE_SERVER_MANAGER_CMD
    CMD_TYPE_GET_SERVER_SET to SERVER_MANAGER

## Slide 10: WorkFlow4
Input:
  MSG_TYPE_MEDIATOR_CMD
    get CMD_TYPE_GET_TOPOLOGY from measurement
Process:
  Store this command, its state
Output:
  MSG_TYPE_NETWORK_CONTROLLER_CMD
    CMD_TYPE_GET_TOPOLOGY to networkController

## Slide 11: WorkFlow5
Input:
  MSG_TYPE_MEDIATOR_CMD
    get CMD_TYPE_GET_NF_STATUE from measurement
Process:
  Store this command, its state
Output:
  MSG_TYPE_DOCKER_CONTROLLER_CMD
    CMD_TYPE_GET_SFCI_STATUE to dockerController