## Slide 1: OpenFlow Router

## Slide 2: Switch-Centric Topology
OvS
OvS
OvS
Ingress
DCN
Web
Server 1
Web
Server 2
OvS
DCN
Gateway 1
BESS
VNF1
Server3
10.1.1.1
Kernel
Server0
SAM
Classifier
Server1
Kernel
OvS
OvS
OvS
OvS
OvS
OvS
Inbound traffic = 2.2.2.2 -> 1.1.1.1
Website DNS IP = 1.1.1.1
2.2.s3.0/27
2.2.s4.0/27
2.2.s1.0/27
DCN
Gateway 2
BESS
VNF1
Server4
Kernel
10.1.1.2
Classifier
Kernel
Server2
2.2.s2.0/27
2.2.s0.0/27

## Slide 3: IP Addressing
Each switch could connect several servers and other switches.
Each switch (which connected with servers) is assign an gateway address: 2.2.[switchID.1].
[switchID] takes up 11 bits, the lower 5 bits is host number.
This addressing support 2048 switches, each switches support 30 servers.
This ip addressing can used to implement fat-tree k=36 (1620 switches and 11664 servers)

## Slide 4: Switch’s Tables
Flow Table 0 – MAIN_TABLE |  | 
Match | Instructions | Priority
dstMAC=LOCAL_PORT_MAC1, etherType=IPv4 | GOTO IPv4_CLASSIFIER_TABLE | 1
dstMAC=LOCAL_PORT_MAC, VLANTag | GOTO VLAN_TABLE | 1
Table-miss | GOTO L2_TABLE | 0
Flow Table 1 – IPv4_CLASSIFIER_TABLE |  | 
Match | Instructions | Priority
IN_PORT=XXX | Set-field: Srcdstmac; GOTO L2_TABLE | 3
dstIP=10.0.0.0/8 | GOTO UFFR_TABLE | 2
dstIP=2.2.0.0/16 | GOTO WEST_EAST_TABLE | 2
etherType=IPv4 | GOTO NORTH_SOUTH_TABLE | 1
Table-miss | PACKET_IN | 0
L2
West-east routing
UFFR
North-south routing
To server based classifier
VLAN routing
IPv4 routing

## Slide 5: Switch’s Tables
Flow Table 3 – NORTH_SOUTH_TABLE |  |  | 
Match | Instructions |  | Priority
etherType=IPv4 | Normal Switch | DCN Gateway | 1
 | TTL; Set-field: srcdstmac; GOTO L2_TABLE | TTL; Set-field: srcdstmac; Outport 1 | 
Table-miss | PACKET_IN |  | 0
L2
West-east routing
UFFR
North-south routing
Flow Table 2 – WEST_EAST_TABLE |  | 
Match | Instructions | Priority
dstIP=2.2.[switchID.1].0/27 | TTL; set-field: srcdstmac; GOTO L2_TABLE | 1
dstIP=2.2.[switchID.2].0/32 | TTL; set-field: srcdstmac; GOTO L2_TABLE | 1
Table-miss | PACKET_IN | 0

## Slide 6: Switch’s Tables
L2
West-east routing
UFFR
North-south routing
Flow Table 7 – L2_TABLE |  | 
Match | Instructions | Priority
etherType=Arp | PACKET_IN | 2
dstMAC=PEER_SWITCH_MAC | Outport X | 1
dstMAC=HOST_MAC | Outport Y | 1
Table-miss | PACKET_IN | 0
Process arp broadcast and
reply default gateway to each host
Flow Table 6 – UFFR_TABLE |  | 
Match | Instructions | Priority
dstIP=10.1.1.1/32 | Group 1 | 1
dstIP=10.1.2.1/32 | Group 2 | 1
dstIP=10.1.2.2/32 | TTL; Set-field: Srcdstmac; GOTO L2_TABLE | 1
Table-miss | PACKET_IN | 0
Flow Table 4 – VLAN_TABLE |  | 
Match | Instructions | Priority
VLANID=XXX | set-field: srcdstmac; GOTO L2_TABLE | 1
VLANID=XXX | PopVLAN; GOTO NotVia_TABLE | 1
Table-miss | PACKET_IN | 0
Flow Table 5 –NotVia_TABLE |  | 
Match | Instructions | Priority
dstIP=10.1.1.1/32 | Group 1 | 1
dstIP=10.1.2.1/32 | Group 2 | 1
Table-miss | PACKET_IN | 0

## Slide 7: Switch’s Tables – UFFR
Group Table |  |  | 
Group Identifier | Group Type | Action Buckets | 
 |  | Bucket 1 | Bucket 2
1 | Fast Failover | TTL; Set-field: Srcdstmac; Outport 3 | TTL; Set-field: dstIP; Set-field: Srcdstmac; Outport 2;
2 | Fast Failover | TTL; Set-field: Srcdstmac; Outport 1 | TTL; Set-field: dstIP; Set-field: Srcdstmac; Outport 2;

## Slide 8: Switch’s Tables – NotVia
Group Table |  |  | 
Group Identifier | Group Type | Action Buckets | 
 |  | Bucket 1 | Bucket 2
1 | Fast Failover | TTL; Set-field: Srcdstmac; Outport 3 | Push-tag: vlan; Set-field: Srcdstmac; Outport 2;
2 | Fast Failover | TTL; Set-field: Srcdstmac; Outport 1 | Push-tag: vlan; Set-field: Srcdstmac; Outport 2;

## Slide 9: Event
Add/del switch
Add/move host
Add/del link
Add/modify/del port
  BUG1: add port 从未成功触发
    Add switch/link/host时不会触发此event
  BUG2: modify/del port可能触发失败
    del switch时不会触发此event
    del link时会触发此event

## Slide 10: L2 app
Update local port entry
  addLocalPort(port)
    isIn localPortTable?
    Add port into localPortTable; add entry
  delLocalPort(port)
    isIn localPortTable?
    Del port from localPortTable; del entry
  Event:
    Add port event: addLocalPort(port)
    Del port event : delLocalPort(port)
    Add switch/link/host event : addLocalPort(port)
    Del switch event :
      del localPortTable

## Slide 11: L2 app
Update peer port entry
  addPeerPort(port)
    isIn PeerPortTable?
    Add port into peerPortTable; add entry
  delPeerPort(port)
    isIn PeerPortTable?
    Del port from peerPortTable; del entry
  Event:
    Add link: addPeerPort(port)
    Del link: delPeerPort(port)
Update host mac entry
  Packet in: arp

## Slide 12: West-East App: Update RIB
Switch：
  旧表组有&&新表组没有：全部删除
  旧表组没有&&新表组有：全部安装
  旧表组有&&新表组有：下一步
Entry
  新entry的match在旧表中:
    删除旧entry，安装新entry；
  新entry的match不在旧表中：安装新entry；
  旧entry的match不在新表中：删除旧entry；

## Slide 13: North-South App:
DCN Gateway switches list.
Set the default outbound of a dcn gateway as port 1.
Get spt to default gateway.
For gateway, set default ipv4 forward entry to outbound port.